## Slide 1: CFL Documentation
Colum Flow Language

## Slide 2: Introduction <next>
In 2005-time frame, the Column Flow Language, CFL was developed for an 8051, to solve the problem of complex sequences and state machines was developed.
The original CFL system was enhanced as the system was employed of various processors and languages. A list of languages include C, Lua, Python and Go.
The CFL system was my default manner to develop application software.
The problem was that there was no standard. Each application had its own implementation. The intent of this presentation is to:
  Present a standard implementation architecture.
    Due to target limitations as well a language details, there will be variances in the implement.
  Document the implementation.

## Slide 3: Introduction <back> <next>
Column Flow Language, which is called CFL for short, is a sequence-based language which encapsulates the control flow of an implementation.
  Attached to the sequence elements which execute a function which is isolated from the control flow of the general task.
  This is done because of two capabilities:
    The capabilities of the enhanced sequence-based language.
    Auxillary functions are introduced which specific call back functions are attached to. Much in the same way that Web frame works intercept browser events and implement call backs for users to attach to these specific actions.

## Slide 4: Introduction <back> <next>
The outline of this document is as follows:
  Historical Development
    This section highlights the ideas which lead to the CFL, Column Flow Language.
  Top Level Architecture
    This section details the top-level architecture:
      Major components
      CFL Engine Operations
  CFL virtual programming language
    This section describes the CFL commands used to construct a system as shown by the following link.
  Auxiliary Functions
    This section lists the default Auxiliary Function of the CFL as shown by the following link.
    Auxiliary Functions are defined in the following manner
      The CFL Engine receives events and sends events to active columns.
      Active columns have column elements
      Attached to column elements are user defined functions.
      Auxiliary functions are much like in a Web environment where browser events are:
        Intercepted by web frameworks and:
        Common functions are handled by the web framework
        User specific events are handled by user supplied functions.

## Slide 5: Introduction <back> <next>
Appendixes
  The current CFL implementations are as follows:
    A. 32k Ram ARM M0 type implementation is shown here.
      This implementation is designed for PLC, Programable Logic Controller type implementations.
      This implementation features very low Ram utilization and is suited for applications where there is a danger where Ram can be corrupted. Either through an external event or through an errant program corrupting Ram.
      The major with this implementation is that the program is difficult to update without reprogramming.
    B. Modified 32k Ram ARM M0 type implementation is shown here:
      This implementation consumes more Ram and Flash but allows updating the program through an I/O device like a MicroSD device.
      The major limitation is that this version cannot update or add auxillary functions and user call back functions.

## Slide 6: Introduction <back> <next>
Introductions continued
  The Lua implementation is design for the higher end microcontrollers with several 100k’s of Ram and Flash as well as Linux controllers with Ram in the 100’s of Meg. There are three implementations starting from the simplest to the more complex. An introduction to these implementations is shown here.
  The Go Lang implementation is show here.
  The Python implementation is shown here. (TBD)
  The Rust implementation is show here. (TBD)
  The Java script implementation is shown here. (TBD)

## Slide 7: Introduction <back>
Introduction ( continued )
  Historical Implementation
    A. Modbus Moisture sensor 2018 implementation shown here.
      based upon a 4k Ram and 32k Flash Arm M0 microcontroller .
      This implementation was done on an older CFL engine in 2018
      This implementation was successfully used in the field for 6 months.
      This example is easy to understand and shows the advantage of the CFL implementation.
  PCL Background information is shown here.
  NASA VML virtual space control controller is shown here.

## Slide 8: Historical Development of CFL, Column Flow Language <back> <forward>
Column Flow Language (CFL) was developed around 2005. The development of CFL was driven by two main factors:
  Nested Complex State machines
    An example of this problem is shown on the following page.
    Nested state machines were found to be extremely fragile:
      Especially when new conditions were introduced to an existing state machine.
      The new condition resulted in changes being propagated up from the lower state to the upper states.
  Handling Sequences: State machines were not efficient at managing sequences.
    A step in a sequence could wait on a condition and :
      If the condition changed then,
      The entire or partial sequence would be aborted.
      This complication is shown on the following page.

## Slide 9: Example of fragile state machine. <back>
Top Level State
Sub State Level 1
Sub State Level 1
Sub State Level 1
Sub State Level 1
Sub State Level 2
Sub State Level 2
Sub State Level 2
Sub State Level 3
Sub State Level 3
Sub State Level 3
Sub State Level 4
Sub State Level 4
Sub State Level 4
Changes here can force changes up the higher-level states

## Slide 10: Complication of Some Sequences <back>
Sequence 1 Condition 1
Sequence 2 Condition 1
Condition 2
Sequence 3 Condition 1
Condition 2
Condition 3
Sequence 4 Condition 1
Condition 2
Condition 3
Condition 4
…
Only One Sequence Step is active at a time. Condition logic for each sequence must be included in the following sequences.

## Slide 11: Historical Development of CFL, Column Flow Language <back> <forward>
The solution to both problems is to define a sequence engine with enhanced properties. The UML for a sequence engine is show in the following link.
A traditional sequence engine executes steps consecutively until the sequence is complete. The enhanced property of the sequence engine is to include the following enhancements.
  The sequence engine will receive events and distribute events to all sequences that are active.
  For each sequence events are sent to each step.
  Each step will return an event code that will affect the event processing for the sequence.
  Based upon the event code, the step will be active or become inactive.
  Also, the return code can affect the sequence engine as described on the next page.

## Slide 12: Historical Development of CFL, Column Flow Language <back> <forward>
  The return codes for the sequence step are as follows:
    A step can terminate the sequence event processing.
    A step can halt the event processing till the next event.
    A step can allow event processing to continue.
    A step can continue processing and disable the step from future events.
    A step can reset the sequence which will result in:
      The set will be terminated
      And then enabled again
    A step can terminate the sequence engine.

## Slide 13: Historical Development of CFL, Column Flow Language <back> <forward>
Using the modified sequence manager, the sequence that was shown in the link can now be transformed to the following form shown below.
The ‘Wait’ condition:
  blocks will wait for the condition to occur
  and then become inactive.
The ‘Verify’ steps will:
  stay active
  monitor the condition.
  If the condition fails, the verify block could either:
    terminate the sequence
    or reset the sequence.
Wait till
Condition 1
Verify till
Condition 3
…
Wait till
Condition 3
Verify
Condition 1
Wait till
Condition 2
Verify till
Condition 2

## Slide 14: Historical Development of CFL, Column Flow Language <back> <forward>
The modified sequence engine can handle state machines in three different ways.
  The first way is to handle a state machine within a sequence by selectively enabling and disabling sequence steps.
  The second way is to dedicate a single sequence for a state. By selectively enabling and disabling sequences, then a simple state machine can be accomplished.
  The first two steps can implement a simple state machines. Complex state machines required extra features to be built into the sequence engine.
Each of these approaches will be described in the following pages.

## Slide 15: Historical Development of CFL, Column Flow Language <back> <forward>
The first mechanism is to control which element is active within a sequence, as shown in the figure below.
By selectively enabling the node with the state, a simple state machine can be implemented.
State A
State F
State E
State B
State C
State D
In this case only the node label State B is active
State A
State F
State E
State B
State C
State D
In this case only the node label State D is active

## Slide 16: Historical Development of CFL, Column Flow Language <back> <forward>
The state machine implemented as a sequence can have additional functions depending on the needs of the developer.
A sequence can have an initial sequence before the state machine as show in the figure on the right.
A sequence can have a final sequence as show in the figure on the right.
Also, a state machine can have common event handlers for each step. These event handlers can be factored out into steps before the state machine as shown on the figure to the right
Common Event Handlers
Initial Sequence steps
Initial Sequence steps
Common Event Handlers
State machine steps
Terminal Sequence steps
Initial Sequence steps
State machine steps
State machine steps
State machine steps
Terminal Sequence steps
Terminal Sequence steps
Steps of the sequence

## Slide 17: Historical Development of CFL, Column Flow Language <back> <forward>
The second mechanism is to dedicate whole sequences to a state.
Changing states means enabling a sequence and then disabling the rest of the sequences
Step 1
Step 6
Step 5
Step 2
Step 3
Step 4
Step 1
Step 6
Step 5
Step 2
Step 3
Step 4
Step 1
Step 6
Step 5
Step 2
Step 3
Step 4
Step 1
Step 6
Step 5
Step 2
Step 3
Step 4
State A
State B
State D
State C
This Sequence is Active

## Slide 18: Historical Development of CFL, Column Flow Language <back>
Complex state machines is implemented by:
  a preprocessor function call
  several specified column element function.
The complex state machine as well as the common state machine will be described under the auxillary function section.

## Slide 19: Top Level Architecture <back> <next>
The CFL architecture is based upon two core concepts. The first core concept is the use of a virtual machine as demonstrated by two NASA virtual machines.
  In the early 2000’s NASA developed, VML, Virtual Machine Language, which has the properties shown in the following link. VML is used in NASA’s large telescope satellites and interplanetary satellites, and fixed landers. The VML system reduces the spaceship control to executing scripts.
  The F’Prime system is a quasi-virtual machine used to control the Mars Helicopter. The link for F’Prime system is here.

## Slide 20: Top Level Architecture Continued <back> <next>
The second core concept is that the CFL virtual machine is based upon columns or modified sequence
  The basis of the CFL is based upon the following concepts:
    The CFL system is driven by events.
    Events contain:
      An event id
      Event can have data attached to the event.
    Events are stored in queues.
      There is a central event queue.
      Event queues can optional be attached to event queue.
  A sequence as defined by the UML specification as shown in the following link.
  The changes to the conventional sequence engine are as follows:
    Multiple sequences can be active at the same time.
    Multiple elements of a sequence can be active at same time.
  A step in a column or modified sequence consist of a data structure which contains function pointers and attached data.
    Step in the sequence are structures which have function pointers and data attached to the structure.
    Events are sent a column and then sent to sequence steps.
    The CFL engine calls functions attached to the sequence steps.
    The function when called, return codes which affect the flow event processing of the column.

## Slide 21: CFL Engine Components <back> <next>
The CFL, Column Flow Language, consists of the following architectural components:
  Event Queues consists of two types
    Global Event Queue
      This Queue receives all system events and external events.
      This queue distributes the events to all the column elements.
    Optional Column Event Queue
      Not all Columns have event queues.
      Events sent to the Column Event Queue are from processing elements of columns.
      Events sent to this type of queue are processed for the local column.
  Columns or Modified Sequences
    Column are the processing elements of the system. As mentioned earlier column entities act like modified sequences.
  Column Elements or Sequence Steps
    Column Elements are processing elements which attach to columns.
A top-level view of these components is shown in the following link.

## Slide 22: CFL Components and Component Relationships <back>
The figure to the right shows the architecture of the CFL System as well as the event flow. Each of the components will be discussed in the next section. However, the language of the implementation is left open. CFL engines have been constructed using C, Lua, Python, and Go.
Global
Event Queue
Timer tick and Calendar Events
Interrupts and other external events
CFL Engine
Optional Column Queue
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Optional Column Queue
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Optional Column Queue
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Optional Column Queue
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Column
Element
Event Flow
From the first column element
to last column element
Event Flow Between Columns
Event Flow Between Columns
Event Flow Between Columns
CFL Engine will send external events to Columns and process the event flow between column elements

## Slide 23: Interface of the CFL engine <back> <next>
The purpose of this slide is to describe the way that the CFL engine interacts with the target environment. As the interaction is shown in the figure to the right.
  CFL code is data structures
  An engine is needed to execute the data structures
  The figure to the right shows the startup and completion status.
  The engine is started by a startup call by a conventional program.
  Multiple CFL engine instances can be instantiated if a multiple thread environment is used.
  When the CFL engine stops, execution returns for the calling program.
  Multiple CFL instances can be run to support various operation of the target environment, where each instance can be run individually or in a consecutive order.
Conventional program
CFL Engine
CFL Data Structure
CFL Data Structure
CFL Data Structure
CFL Data Structure
CFL Compiler
User Scripts
Event Data const of
Unique Event Id
Data pointer to data

## Slide 24: Description of CFL components <back>
The components of the CFL system are as follows:
  Events
  Event Queues
  Columns
  Column Elements
  Column Elements Function API

## Slide 25: CFL Events <back>
Events have the following properties:
  The format of the event is left up to the local architecture.
    However, each event will have a unique ID.
    The type of the unique ID is left up to the local architecture to define, i.e., it could be a char, integer, or even a string type.
    The event also beside an event id can contain attached data. The attached data has no defined format.
The CFL system is a discrete system.
  Timer ticks are sent to active columns.
  The timer tick allows continuous processes to be modeled as a discrete control system
  Calendar events such as seconds, minutes … are sent to active columns

## Slide 26: CFL Event Queues <back>
Event Queues are queues where events are stored in a queue which operates on a first-in, first-out basis.
There are two types of event queues.
  There is one global event queue. Events from this queue are sent to all columns.
  Columns can optionally have event queues.
    Events sent to column event queues are processed only by the column.

## Slide 27: CFL Columns <back>
Columns are lists that:
  Hold column elements in a linear fashion.
  Send events to each column element, starting from the first to the last.
  Process events and return a code which affects subsequent event processing.
  Optionally contain an event queue exclusive to the column's elements.
  Have two attributes:
    A Boolean indicating whether the column is active. Inactive columns do not receive events.
    A Boolean indicating whether the column is enabled at startup. Note: if no column is active at startup, no processing occurs.

## Slide 28: CFL Column Elements <back> <next>
A column element is attached to a column. Attached to each column element is a function which receives the event and returns.
Each column element has two attributes:
  A Boolean indicating whether the element is active.
  A Boolean indicating whether the element has been initialized.
When a column is initialized:
  The 'active' attribute of all column elements is set to true, making the column element active.
  The 'initialized' attribute of all column elements is set to false, marking them as uninitialized.
When a column is active, the column receives events from two sources.
  From a single global queue
  From an optional event queue attached to the column element.
For each event, the CFL engine sends events to each active column element from the first to the last.
If multiple events are required by the function to complete, the function must maintain local state variables for the function.

## Slide 29: CFL Column Elements (Continued) <back>
The function returns one of six return codes as described on the next page.
Column Element Return Codes
  Upon receiving an event, column elements return one of the following codes:
    Continue: The element remains active, and processing moves to the next column element.
    Disable: The element becomes inactive and will not receive future events. Processing continues to the next column element.
    Halt: Processing stops, but the column element remains active.
    Terminate Column: Processing stops, and a terminate event is sent to the column. (Refer to the next section for details.)
    Reset Column: A combination of Terminate Column and Enable Column. (Refer to the next section for details.)
    Terminate Engine: Stops processing and returns control to the calling program.

## Slide 30: CFL Basic Documentation /Top Level Architecture <back> <next>
The API of the column element is a follows:
  <Return Code> function( <handle>, <auxiliary function>,<parameters>, <event data>)
  The type of the <return code> which is usually a form of the integer.
    Return codes were discussed in the previous page.
  The handle is like a file handle in conventional programming languages, which is used to access CFL engine library calls.
  The <auxiliary function> and <parameters> allow construction of modular column element functions. This capability will be discussed in later slides.
  The <event data> is the event data which is passed to the column element function. <event data > is usually a structure or record which holds the event ID and attached data.

## Slide 31: CFL Basic Documentation /Top Level Architecture <back>
The Column Element Function receives events from the column engine.
The CFL system has two pseudo events which are sent to column element functions:
An initialization event:
  When a column element that has not been initialized, a reset event is sent to the column element and then the initialization attribute of the column element is set to true. The return code from the column element is ignored. The initialization event allows the column element to perform one-time initialization tasks such as initializing counters or allocating dynamic memory.
A termination event:
  A termination event is sent to a column element under two conditions:
  When a column element has been disabled. A termination event is sent to the column element and the return code from the column element is ignored. The termination event allows tasks like releasing dynamic memory to be done.
  When the column has been terminated. When the column has been terminated, the column elements are processed from the bottom to the top. Column elements which are both active and initialized are sent the termination event. Column elements which are active and not initialized have not started processing.

## Slide 32: CFL Virtual Programming Environment <back> <next>
Introduction
  The CFL virtual programming environment consists of two components.
    Programming statements
    An assembler which takes the programming states and generates tables.
  There are two programming environments as shown in the following figure.
    An offline environment
    An online environment
  Both environments have the same logical steps:
    CFL source statements
    CFL assembler
    Results of the Assemble
    CFL engine.

## Slide 33: Two CFL Development Contexts <back>
Offline Development
Online Development
Source Code
Text Files
CFL Assembler
Offline Program
CFL Tables
CFL Engine
Offline
Target Environment
Source Code
Programming Statements
CFL Assembler
Function Calls
CFL Tables
Data Structures
CFL Engine
Environment
Totally Contained
In Target System

## Slide 34: CFL Virtual Programming Environment <back> <next>
Introduction (Continued)
  The differences can be summarized as follows:
    CFL source statements
      Offline – Text file
      Online – Programming Statements
    CFL assembler
      Offline – A script base assembler like Python or Lua
      Online – Function calls
    Results of the Assemble
      Offline – A data file like a .h file
      Online – Data structures in target environment
    CFL engine
      In both environments this is a set of function calls in the target environment

## Slide 35: CFL Virtual Programming Statements <back> <next>
The virtual language statements are valid programming statements.
The statements are as follows:
  For the offline environment, the programming language is in the language of the CFL assembler.
  For the online environment, the programming language is in then language of the target environment.

## Slide 36: CFL Statement Classes <back>
The CFL programming statements can grouped into the following classes.
  Definition of Resources -- statements are defined by following link.
  Definition of Columns -- statements are defined by following link.
  Definition of Column Elements – statements are defined by following link.
  Miscellaneous Statements -- statements are defined by following link.
  The offline environment requires native code to defined in CFL statements uses appropriate CFL functions.
    The native code is entered as text.
    A template engine has been developed which assists in specifying native code.
    The template engine allows binding parameters in the CFL code to the native code for parameters like event ids and other constants.
    The template engine is specified here.

## Slide 37: Definition of Resources <back> <next>
The CFL language requires resources be defined before being used.
Many resources are subsystem dependent and will be introduced when the subsystems are defined. Among the subsystems are:
  Subsystems required for PLC, Programable Logic Control problems.
  Complex State machines
  The CFL assembler is script driven and subsystems can be added into the system depending upon user requirements.

## Slide 38: Definition of Resources Continued <back>
One resource command that is required for any CFL build is define_columns
  define_columns(column_list)
  column_list is a list of columns that comprise the build.
  This command solves four problems.
    The first problem is a forward reference problem where a column is referenced before the column is defined.
    The second problem is that at the end of a build all required columns are defined.
    The third problem is that unexpected column names are flagged as an error.
    The fourth problem is that this command solves which columns get events first.
      The event distribution to columns follows the order of the column list.
      In general, use of the ordering of column events to do processing should be avoided.

## Slide 39: Definition of Columns <back>
A column definition is shown in the following figure.
The define_column command starts the column definition process.
  The parameters are:
    Column name
    Auto start flag – true means that the column is active at start up.
    Queue_name – specifies the name of the event queue which is attached to the column. For a Lua implementation a nil means that no column queue is attached to the column.
The end_column command terminates the definition of the column.
  This command has no parameters.
Commands between the define_column and the end_column are called column elements.
  For the column elements shown in this example are auxillary functions. auxillary functions will be discussed in the next section.
Column elements are added to a script after a define_column and before an end_column.
Similarly, a define_column can not be issued until and end_column has been issued.
A column name can be entered only once for a define column.

## Slide 40: How to define a column <back>
Example of a column definition is shown below.
  The CFL language was Lua
  The target CFL system is C environment with Low Ram resources.
  The CFL code for a column is shown below.
define_column("start_column",true,nil)
Log_msg('start column')
Enable_columns({table.unpack(enable_columns)} ,false)
Log_msg('terminating system')
terminate_column()
end_column()

## Slide 41: Definition of Column Element <back> <next>
A column function produced a data structure which has two functions pointers and a pointer to user_data
Defining a column element is implementation dependent.
For the CFL C Low Ram implementation, the Lua command to enter a column command is as follows:
  function store_column_element(column_function,aux_function,user_data)
  column_function is string name of the c function.
  aux_function is a string name for the c function which is used as a call back function to extend the range of activities of the column_function.
  User_data is the name of the data structure that is based to the column function.
This command is rarely used as user command.
Rather aux_functions are used which simplify adding column elements

## Slide 42: Definition of Column Element <back>
Two of the parameters in the column element can have different types depending upon the implementation of the column element.
  The aux_function and definitely the user_data parameter will have different types.
In the C implementation void * pointers are used to store pointers.
In Go interface{} parameters are used to implement pointers.
In Lua and Python type less parameters are used to implement parameters.
For Rust, the details have not been worked out.

## Slide 43: Definition of Miscellaneous Statements <back>
Note the examples are from the Lua base c low ram target
Miscellaneous commands are commands that is used to:
  Control CFL assembly process
    set_h_file("float_maps_1.h")
      This commands specifies the output file for the CFL assembler
    dump_build()
      This commands signals to the CFL assembler to stop specifying and start the assembly process.
  Specify parameters to configure the runtime environment.
    start_build(..)
      This command specify information on parameters such as
      Definition structure name
      Size of heaps (CFL c low ram system uses private heaps)
      Debug function name
      .. Other parameters as needed
  For offline systems, user defined code is defined and assembled with specialized commands

## Slide 44: CFL Aux_functions. <back> <next>
Aux_functions are functions that make defining column elements easy.
  As a note column elements are discussed here.
The function to define column elements is of the form:
  function store_column_element(column_function,aux_function,user_data)
    Function is discussed here.
When defining column elements, the user has to match the parameters of the aux_function and the user data which is
  Time consuming
  Error prone
Also, there is repeated actions which could be modularized into a function that reduce programing steps and reduce errors

## Slide 45: CFL Auxiliary Functions. <back>
The auxiliary Functions can be broken down into the following categories.
Main auxiliary Functions
  Basic functions
  Column Queue Events
  While/verify
  Watch Dog
  Time of Day
  Column Control
  Column Data
  Column State Machines
Added features
  RPC services
  CFL s expression arrays
  Complex State Machines

## Slide 46: Basic Helper Functions <back>
The basic helper functions can be organized into the following groups
  Return codes – Link here
    A column element function can return one of 6 return codes as shown in this link.
    These function singular purpose is to return one of these 6 return codes.
  Diagnostic Message – Link here
    The debugging of CFL systems is some times difficult to do with break points
    Having a log message with the following properties was found useful.
      The id of the column
      The id of the column element
      A diagnostic message
  Events – Link here
    Events are sent to two types of queues.
      The first type is the global queue where the event is sent to all columns
      The function that sends the event to the global queue is discussed in this section.
      The function that sends events to column queues is discussed in this link.
  One shot functions – Link here

## Slide 47: Return Codes <back>
The return code functions are:
  terminate_engine()
    Returns a Terminate Engine return code which immediately shuts the CFL engine down.
  reset_column()
    Return a Reset Column return code which resets the column, and the column is set to and active state.
  terminate_column()
    Returns a Terminate Column return code. Active column elements are sent the pseudo event, Terminate and then the column is set to a inactive state.
  halt_column()
    Return a Halt Column return code. The event processing in the column is halted and the column remains active.
Examples of use
  This column terminates engine after 10 seconds
  define_column("column4",true,nil)
    Log_msg( 'test_terminate_engine')
    Wait_delay(10000)
    Log_msg( 'column 4 is terminating engine after 10 seconds')
    terminate_engine()
    end_column()
  This column sends a global event, waits 2 seconds and then resets the column, which causes another cycle of sending the event and waiting
  define_column("column1",true,"queue1")
    Log_msg("this is a test message")
    send_global_event(test_def)
    Wait_delay(2000)
    Log_msg("reseting the column every 2 seconds")
    reset_column()
    end_column()

## Slide 48: Diagnostic Message <back>
The diagnostic log message for the CFL system is
  Log_msg( ‘display message’)
  This message will display on the debug output text stream of the CFL system.
  The debug output stream function is passed when the CFL system initializes.
  The display message has the following information.
    On some like Arduino, the time stamp is displayed
    The column id
    The column element id
    The display message

## Slide 49: Send Global Event <back>
The function to send an event to the global queue is as follows:
  send_global_event(<event>)
  On configurations where the CFL assembler is running on the target system the event is usually a map or hash.
  On configurations where the CFL assembler is not on the target system then the event must be constructed by a CFL assembler command.
    For the CFL c low ram system the commands to construct an event is:
      add_user_event("test_event")
        Register “test_event” and generate an integer event id.
      test_def = generate_event(get_event("test_event"),false, '( void *)user_test_event_data’)
        Where generate_event(event_id, malloc_flag, user_data_address)
          event_id is the unique event id
            Note if the event id is not unique an error will occur.
          malloc_flag is Boolean and signals whether the user_data has been dynamically allocated.
            The CFL engine will free the memory after the end of processing.
          User_test_event_data is a void pointer which will be cast to a valid pointer by the appropriate column element function.

## Slide 50: One Shot Functions <back>
One shot functions are functions that:
  Do an action and then emit a return code which disables the column element.
    The function is the One_shot_function which is described here.
    An example of this type of action is:
      Diagnostic Message
      Send Global Event
    These functions call the One_shot function which calls the function to store the column element which is discussed here.
  Do an action and then when the column element is being terminated do a second action.
    The second the One_shot_terminate_function which is described here.
    An example of this is to allocate memory and free the respective memory when the column element terminates.

## Slide 51: One_shot_function <back>
The One_shot function is defined as follows:
  One_shot(<user_function>, <user_data>)
The operation of the one_shot function during execution is as follows:
  The interface for a column element function is a as follows:
    <return code> function(<handle>,aux_function, user_data,<event_data>) see link.
  For the one_shot function the function interface is as follows:
    (<handle>,user_function, user_data,<event_data>)
  The runtime code for the code handles the CFL event flow in the following manner.
    The runtime code first receives the pseudo initialization event.
      The aux_function, which is the user function is called with same parameters.
      This allows the initialization action to occur.
    The runtime code then returns a Disable return code which removes the column element from event processing.

## Slide 52: One_shot_terminate_function <back>
The One_shot_terminate function is defined as follows:
  One_shot_terminate(<user_function>, <user_data>)
The operation of the one_shot function during execution is as follows:
  The interface for a column element function is a as follows:
    <return code> function(<handle>,aux_function, user_data,<event_data>) see link.
  For the one_shot_terminate function the function interface is as follows:
    (<handle>,user_function, user_data,<event_data>)
  The runtime code for the function code is as follows.
    The runtime code first receives the pseudo initialization event.
      The aux_function, which is the user function is called with same parameters.
      This allows the initialization action to occur.
    The runtime code then returns a Continue return code for all events except for the pseudo event Terminate.
      The aux_function, which is the user function is called with the same parameters.
      This allows the termination action to occur.
      The aux_function, which is the user function, must branch on the initialization and termination event to determine whether initialization or termination action is to be done.
    Also, note a termination event will not be issued a column element unless the column element is initialized. When a column element is initialized, then the column element will have received the pseudo initialization event. This insured, that the termination actions will not be called before initialization actions.

## Slide 53: Column Queue Events <back> <next>
  The CFL assembler command to define a column is:
    define_column(column_name, startup_flag, queue_name, size )
      The parameter column name is the name of the column
      The startup_flag determines where the column is active at startup
        True means that the column is active at startup
        False means that the column is not active
      The parameter queue_name is the name of the queue associated with the column.
        If a nil or no parameter is specified, then no queue is attached to the column.
        If a name is specified, then a queue which is attached to the column. Both column_name and queue_name must be unique for the build, or an error is created.
      The parameter size is the size of the queue.
        If no parameter is specified, then the size of the queue is 10.

## Slide 54: Named Event Function <back> <next>
The function which sends events to the column queue is:
  send_queue_event(column_queue, event)
  where:
    The parameter column_queue is the name of the column_queue
    The parameter event is the event data that is sent to the column queue.
    The parameter event is generated by the CFL assembler function:
      generate_event(get_event("filter_event"),false, 'NULL’)
      Which was discussed here.

## Slide 55: Difference between Column Queue Events and Global Events <back>
The motivation for named queue events is as follows:
  Global events are sent to every column for processing.
    This is a waste as in many cases only one column is interested in the event.
    The exception is events like time ticks and calendar events. Virtually all columns need the time tick event.
Column queue events are sent specificity to a unique column.
  This makes the event processing more efficient as well as more modular.

## Slide 56: While/verify functions <back> <next>
  The While and Verify functions are a useful pair of functions for implementing column actions.
    The while function waits on a condition.
      If the condition does not occur, then the column element emits a “Halt return” code and stops event processing
      If the condition does occur then a “Disable return” code is emitted, and the column element is disabled, and the event processing continues.
      On a timeout error, the option is provided to either disable the column or reset the column.
      The while function has an optional time out with an optional error call back function to do addition user require actions.
    The verify function verifies that a condition occurs.
      If the condition does not occur, then there is the option of resetting the column or disabling the column.
      On error, there is an optional callback function to do additional user defined actions.

## Slide 57: While/verify functions Continued <back> <next>
The use of the while/verify commands are used in a pair as shown below:
  define_column()
    -----
    ----
    wait(…)
    verify(..)
    -----
    -----
    end_column()
This action waits for a condition and verifies that the condition remains true during the operation of the column

## Slide 58: While/verify functions Continued <back>
Both the While command and the Verify command through the use of high-level helper functions can generate many additional functions such as:
  Wait for time delay
  Wait for event counts
  Other subsystems, like Bit Maps will use the wait and verify functions to build higher level systems
The description for the While command is here.
The description for the Verify command is here.

## Slide 59: Wait <back> <next>
The format for the helper function is as follows:
  Wait(condition_fn, time_out_ms, terminate_flag, one_shot_time_out_fn, user_data)
  The parameters are as follows:
    condition_fn – is a user supplied Boolean function which will be discussed later
    time_out_ms is the time out for this condition to occur.
      A time out of 0 means an no time out on the wait condition
    terminate_flag is a Boolean where:
      True means terminate the column
      False means reset the column
    one_shot_time_out_fn – Is a user supplied function to be called in the event of error.
      The function is like the user supplied one shot function in the one_shot helper function.
    User_data -- Is user supplied data. This data structure is used by the condition function and the time out function.

## Slide 60: Wait (Continued) <back> <next>
The condition function for the Wait command is a Boolean function which has the following prototype:
  <Boolean> fn(<handle>,<user_data>,<event_data>)
    This function receives both CFL pseudo events of “init” and “terminate”.
    This allow for:
      Initialization of variables
      Allocation and freeing of dynamic memory.
    If the function returns false, then the wait column element will check time out conditions.
      If the time out did not occur, then the column element function will issue a “Halt” return code, which will stop the event processing.
      If the time out occurred, then the column element will call and optional “One Shot” error function with the following parameters:
      <void> fn(<handle>,<user_data>,<event_data>)
      Note that <user_data> data structure is shared for both the user supplied Boolean and function and the optional error function.
      If the termination flag is true, then the column element will return a “Column Terminate” return code, other wise, the column will issue a “Column Reset” return code.
    If the function returns true, then the column element will issue a “Disable” opcode and this action will allow the event processing to proceed.

## Slide 61: Wait (Continued) <back>
Helper functions will be built around the Wait command much like the One_Shot command. Many of the CFL subsystems are build upon the Wait helper command and well be described later.
There are two general purpose helper commands build upon the Wait commands. The commands are:
  Wait_event_count – described at this link.
  Wait_delay – described at this link.

## Slide 62: Wait_event <back>
The Wait_event helper function has the following prototype:
  Wait_event(event_id, number_of_events, time_out_ms, terminate_flag, time_out_fn, user_data)
This function will block until the <number_of_events> of <event_id> have occurred.
This command inserts a CFL compiler generated Boolean the is inserted in the underlying wait command.
The parameters time_out_ms,terminate_flag, one_shot_function and user_data are the same as the Wait command.

## Slide 63: Wait_delay <back>
The Wait_delay command has the following prototype.
  Wait_delay(<time_delay_ms>)
  This helper command is built upon the Wait helper command.
  Since the time delay will always occur, then there is no need for the other parameters of the Wait command like terminate_flag, time_out, time_out_fn and user_data.
  This command blocks until the desired time delay has been achieved or exceeded.
  The accuracy of the command is dependent on the granularity of the system time tick.
  This command, if possible, uses the system clock for measuring time delay.

## Slide 64: Verify <back>
The verify helper function has the following prototype.
  function Verify(bool_fn, terminate_flag, optional_error_fn, user_data)
  The parameters of the Verify helper command are like the parameters of the Wait command which are show in this link.
  The action of the Verify command is as follows.
    If the bool_fn returns True, then the command emits a “Continue Opcode”. The column element remains active, and the event processing continues.
    If the bool_fn returns False, then the column element emits a “Terminate_Column” or a “Reset_Column”, depending upon the value of the terminate command.
    Also, if the optional one_shot_error function is present then the function is called with associated user_data.

## Slide 65: CFL Watch Dog <back> <next>
The CFL Watch Dog functions ensure that an activity on a column will complete within a specified amount of time.
There are two helper functions which allow this function to occur.
  The first helper function is attach_watch_dog_handler which sets the watch dog handler.
  The second helper function is detach_watch_dog_hander which clears the watch dog function.
  These functions will be discussed on the next page.
There can be only one attach watch dog hander function active at one time. A second attach_watch_dog_handler will over right the values of the first watch dog handler.
There can be multiple attach/detach pairs in a column but only one attach/detach pair can be active at a time.
Also, both the attach/detach functions are built on the one_shot command. Once a column event reaches the detach function, the watch dog is removed. The watch dog command primarily works for column elements that are blocking waiting for a function to occur, like the Wait command. However, the Wait command already has a watch dog function built into the column element command.

## Slide 66: CFL Watch Dog <back> <next>
The prototype function for attach_watch_dog_handler is shown here.
  attach_watch_dog_handler(
    <time out ms>,<reset_flag>,<error_fn>,<user_data>)
  The parameters are the like the Wait command where the watch dog activity must be cleared by the detach watch dog command.
The prototype function for the detach watch dog is:
  detach_watch_dog_handler()
Several use cases are shown in the following pages.

## Slide 67: Watch Dog pass condition <back> <next>
A Watch Dog Case that passes with the watch dog not activating
define_column("watch_dog_pass",true,nil)
Log_msg("watch_dog_pass")
attach_watch_dog_handler(5000,true,error_function,user_data)
Wait_delay(1000)
detach_watch_dog_handler()
Wait_delay(5000)
Log_msg("watch_dog_pass passed")
terminate_column()
end_column()

## Slide 68: Watch Dog Error conditions <back>
A Watch Dog example that generates a Terminate Column
define_column("watch_dog_reset",true,nil)
Log_msg(“will see this message again")
attach_watch_dog_handler(5000,
  true,error_fn,user_data)
Wait_delay(10000)
detach_watch_dog_handler()
Log_msg("should not see this message")
terminate_column()
end_column()
A Watch Dog example that generates a Reset Column
define_column("watch_dog_reset",true,nil)
Log_msg(“will see this message every 5 seconds")
attach_watch_dog_handler(5000,
  false,error_fn,user_data)
Wait_delay(10000)
detach_watch_dog_handler()
Log_msg("should not see this message")
terminate_column()
end_column()

## Slide 69: Time of Day <back> <next>
  The time-of-day functions allow waiting on calendar values.
  Calendar values are defined as follows:
    year
    doy – day of year
    month
    day – day of month
    dow – day of week
    hour
    minute
    Second

## Slide 70: Time of Day <back> <next>
Time of day functions support the following comparison operations:
  Less than
  Less than equal
  Equal
  Greater than equal
  Greater than

## Slide 71: Time of Day <back> next
There are two basic helper functions:
Wait_tod blocks until the time of day occurs. This helper function is built upon the Wait helper function. There are no error conditions as a relevant time of day test will eventual valid.
  The function prototype for Wait_tod is:
  Wait_tod(op_type,dictionary)
    The parameters are as follows:
      op_type is the operator type.
      dictionary contains data for the time-of-day comparison.
  The user does not normally use this function as:
    The dictionary for time-of-day comparisons are built with helper functions
      The dictionary object is built with helper functions described here.
    The op_type parameter is hidden with these helper functions:
      Wait_tod_gt(dictionary)
      Wait_tod_ge(dictionary)
      Wait_tod_eq(dictionary)
      Wait_tod_lt(dictionary)
      Wait_tod_le(dictionary)

## Slide 72: Time of Day <back>
Verify_tod verify that time of day comparison is valid. This function is built upon the Verify command.
  The function prototype for Verify_tod is:
  Verify_tod(op_type,terminate_flag,
    failure_function,user_data,dictionary)
    The parameters are as follows:
      op_type is the operator type.
      terminate flag
        true terminate the column on failure and
        false Reset the column on failure
      Optional failure function to be called on failure
      user_data – data for optional failure function
      dictionary contains data for the time-of-day comparison.
  The user does not normally use this function as:
    The dictionary for time-of-day comparisons are built with helper functions
      The dictionary object is built with helper functions described here.
    The op_type parameter is hidden with these helper functions:
      Verify_tod_gt(terminate_flag,failure_function,user_data,dictionary)
      Verify_tod_ge(terminate_flag,failure_function,user_data,dictionary)
      Verify_tod_lt(terminate_flag,failure_function,user_data,dictionary)
      Verify_tod_le(terminate_flag,failure_function,user_data,dictionary)
      Verify_tod_eq(terminate_flag,failure_function,user_data,dictionary)

## Slide 73: Time of Day (Time comparison dictionary) <back>
Time comparisons are done through a comparison of parameters in a dictionary or hash map.
The time comparison dictionary is not built manually but through helper functions.
The time comparison dictionary is first created with the following function.
  time_dictionary = generate_tod_dictionary()
  At this point there are no comparisons
Time comparisons are added by the calling the following helper functions.
  add_day_of_year(time_dictionary ,day_of_year)
  add_month(time_dictionary ,month)
  add_day(time_dictionary ,day)
  add_dow(time_dictionary ,dow)
  add_hour(time_dictionary ,hour)
  add_minute(time_dictionary ,minute)
  add_second(time_dictionary ,second)

## Slide 74: Column Control <back>
Column Control helper functions start and terminates columns. The helper functions are shown below:
  Enable_columns(column_list,terminate_flag) – link here.
    This command enables a list of columns
  Disable_columns(column_list) – link here.
    This command disable a list of columns
  Join_columns(column_list,terminate_flag) – link here.
    This helper function waits until a list of columns terminates.
  If_then_else_columns(bool_function_name,user_data,then_columns,else_columns,join_flag,terminate_flag)
    – link here.
    This helper function selectively a then or else list of columns based upon the value of a Boolean function.
  While_handler(bool_function_name,user_data,column_list) – link here.
    This helper function repeatedly starts and waits for column to terminate based upon the value of a Boolean function.
  Try_handler(try_function_name,column_list,invert_flag,user_data)
    – link here.
    This function controls the sequencing a column list with a user supplied function.

## Slide 75: Column Control (Enable_columns) <back>
The Enable_columns enables a list of columns and optionally terminates the list of columns if the parent column terminates. The Enable_columns helper command has the following prototype.
  Enable_columns(column_list,terminate_flag)
    column_list is a list of columns which are to be enabled.
      Important note – the column_list can not contain the current column that the helper function was called from
    The terminate flag serves the following purpose.
      If the flag is true, then the columns in the column list are terminated when the column containing the helper command is terminated.
      If the flag is false, then processing for this helper command terminates.
    The helper command Enable_columns (column_list, true) is built upon the command One_shot_terminate which is shown here.
    The helper command Enable_columns(column_list,false) is built upon the command ) One_shot which is shown here.
  There two additional commands which are syntax sugar commands.
    Reset_columns(column_list,terminate_flag)
      This command is Enable_columns(column_list,terminate_flag)
    Chain(column_list)
      This command is Enable_columns(column_list, true)
      This command is modeled after Basic Language command of chain.

## Slide 76: Column Control (Disable_columns) <back>
The helper command Disable_columns disables a list of columns. This command uses the following prototypes
  Disable_columns(column_list)
    Where column_list is a list of columns to disable.
This command is built upon the One_shot command as shown in this link.

## Slide 77: Column Control (join_columns) <back>
This command waits until a list of columns terminate. This command is based upon the following prototype.
  Join_columns(column_list, terminate_flag)
  The parameter column_list is the list of columns waiting to terminate.
  The parameter terminate_flag has the following results.
    If the parameter is true then the columns in the column list will be terminated as the parent column has been terminated.
    If the parameter is false, the columns in the column list will not be terminated if the parent column is terminated.

## Slide 78: Column Control (if_then_else) <back>
The if_then_else_columns allows if/then/else actions to be performed on CFL columns. The prototype for this function is shown below:
  if_then_else_columns(bool_function_name,user_data,then_columns,else_columns,join_flag,terminate_flag)
  The parameters are as follows:
    bool_function -- a function of the prototype:
      <bool> xxx( <handle>,<data>,<event>)
      The then_columns are activated if the function returns true.
      The else_columns are activated if the function returns false.
    user_data is the data passed to the bool_function
    The parameters <then_columns> and <else_columns> have been previously defined.
    The join_flag is a flag to determine if the command waits until the columns activated have terminated.
    The terminate_flag determines whether the columns are terminated if the parent column is terminated.

## Slide 79: Column Control (while) <back>
The while command allows repeated actions to be done for CFL columns. The prototype is shown below.
  while_handler(bool_function_name,user_data,column_list)
  The parameters are as follows:
    The bool_function has the following prototype:
      <bool> xxx( <handle>,<data>,<event>)
      The column_list is activated if the function returns true. The column element returns “Halt” and the event processing down the column chain stops.
      The column_list is not activated if the function returns false. In this case the column element returns “Disable” and event process down the column chain.
      The user_data parameter is used as data for bool function.
  The while_handler waits until all activated columns are terminated before the next decision test is done with the bool function.
  Also, if the parent column is terminated then the activated columns are terminated.

## Slide 80: Column Control -- Sequence Columns <back> <next>
There are cases where columns are to be sequenced based in a controlled manner. There are two helper functions.
  The first helper function is try_handler. This commands sequences the columns based upon the results of the current column being sequenced.
  The second helper function sets the state of the column being sequenced.
The second helper function will be discussed first. The prototype for the second helper function is:
  set_column_return_code(return_code)
  Where return_code is a Boolean

## Slide 81: Column Control – Sequence Columns Continued <back> <next>
The second helper function is try_handler. . The prototype of this function is shown below:
  try_handler(try_function,column_list,invert_flag,user_data)
The try_handler will sequence a list of column elements.
  For each sequenced column, the return code from the sequence column is examined.
    Note the return code from the sequenced column is set by the first column is set by the first helper function.
  If the invert_flag is set to false, the sequencing will stop when the return code of the sequence column is false.
  If the invert_flag is set to false, the sequencing will stop if the return code is true.
  The importance of the invert flag is discussed here.
  The action of the try_function is discussed next.

## Slide 82: Column Control – Importance of invert_flag <back> <next>
Invert flag is false
This situation is used to find the first case where the condition is true.
The columns are sequenced until the desired situation is achieved or the column list is exhausted.
Invert flag is false
This situation is useful for testing. In this case the column return code that returns false will terminate the sequencing.

## Slide 83: Column Control – Sequence Columns Continued <back>
The user supplied function try_function is called after the column sequencing has been completed. The purpose of this function is to attach user actions to the sequencing. The prototype of the function is as follows:
  Try_function( <handle>, Try_data_structure *data);
  Where this function:
    Returns no data
    Try_data_structure is a data structure that is implementation dependent. The data structure will have the following items.
      List of columns
      User supplied data for the function.
      The final state of sequence, either true or false.
      The last step of sequencing.

## Slide 84: Column Data <back>
The sequencing helper functions allowed a Boolean value to be attached to a column to facilitate sequencing. Sometimes application programs need more data.
The helper function Store_column_data allows data to be stored in a list of columns. The prototype for the function is shown below.
  Store_column_data(column_list ,column_data)
  The parameter column_list is a list of columns.
  The parameter column_data is implementation dependent but for language c, column data would be cast to a void * pointer.
The following runtime commands allow column data to be retrieved.
  store_local_column_data
  retrieve_local_column_data
The Try_function as shown here, could use these run time command.

## Slide 85: Column State Machines <back> <next>
Column State machines have been previously defined as a concept here. This section details the definition of column state machines and the functions that interact with them.
There are two CFL assembler instructions. These instructions mark the area where a column state machine start and end. There can only be one column state machine in a column.
  Set_column_state_machine_start() – marks the start of the column state machine.
  Set_column_state_machine_end() - marks the end of a column state machine.
There are one CFL helper functions:
  Change_column_state(new_state) – this helper changes the state of the column state machine. This helper function can only be used in the column of the local state machine.
And one CFL Engine function:d
  change_local_column_state_CFL(input, new_state) – this is the runtime command for changing column state. Code in the target language can call this code to change column state.

## Slide 86: Figurative Construction of Column State Machine <back> <next>
define_column("test_sm_structure",true,nil)
  Log_msg("executing a sequence of actions first")
  Log_msg("action 1")
  Wait_delay(1000)
  Log_msg("action 2")
  Wait_delay(1000)
  Log_msg("action 3")
  Change_column_state(0) -- setting initial state
  --- these are event filter
  store_column_element('filter_event_1','NULL',"(void *)&filter_event_data_1")
  store_column_element('sm_0','NULL',"(void *)&sm_0_data")
  Set_column_state_machine_start()
  store_column_element('sm_1','NULL',"(void *)&sm_1_data")
  store_column_element('sm_2','NULL',"(void *)&sm_2_data")
  store_column_element('sm_3','NULL',"(void *)&sm_3_data")
  Set_column_state_machine_end()
  Log_msg("end step")
  halt_column()
end_column()
The text to the right shows a figurative definition of a column with a column state machine.
Note the helper command, store_column_element. This command allows functions in the target language to be inserted into the column elements. This command is discussed here.
There are 5 sections highlighted by different color.
  Orange, an optional initialization sequence.
  Green, the statement which sets the initial state of the column state machine. This statement is required so that the column state machine will initialize.
    Note the column state could have been initialized by the runtime CFL function
      change_local_column_state_CFL by a native function call.
  Blue, this section is for handling events common to all state machines. By handling the same events in one area makes code maintenance much easier.
  The fourth area is the construction of the column state machines. This section will be discussed on the next page.
  Red, the fifth area is column elements that are after the column state machines. Not sure what the use of this section would be.

## Slide 87: Column state machine layout. <back> <next>
The Layout of the column state machine is shown next.
Note column states are referred to numbers starting from 0.
  Note the functions ‘sm_0’ to ‘sm_3’ which references the states 0 to 3.
The step is to define the first column state.
  This is the store_column_element with the function ‘sm_0’
The start of the state machine is done by the function, which is done after the column state element has been defined:
  Set_column_state_start()
All the column states are defined.
The last step is to mark the end of the column state machine with the:
  Set_column_state_machine_end()
store_column_element('sm_0','NULL',"(void *)&sm_0_data")
Set_column_state_machine_start()
store_column_element('sm_1','NULL',"(void *)&sm_1_data")
store_column_element('sm_2','NULL',"(void *)&sm_2_data")
store_column_element('sm_3','NULL',"(void *)&sm_3_data")
Set_column_state_machine_end()

## Slide 88: Column Element Event Flow <back> <next>
This section describes the event flow during a column state change.
As stated earlier, column state changes are made by calling the runtime command:
  change_local_column_state_CFL(<handle>,new_state)
The user should in the native code issue a return call of “Halt” because:
  The enable and attributes of the column elements have changed.
  predictable event processing will occur when the next event occurs.
Note the value of the new_state is not checked. If an invalid value of new_state occurs then a run time error is issued.

## Slide 89: Initialization and Termination Event During State Change <back> <next>
The pseudo initialization and termination events are sent the column elements during state change.
When a column element of a particular state is enabled, a pseudo initialization event is sent to the column element.
  This allows column elements to be enabled.
  The additional column can be substates.
When a column element of a particular state is disabled, a pseudo termination event is sent to the column element.
  This event allows the substates, represented by columns to be terminated.

## Slide 90: Column State Machines Summary <back>
The column element state machine offers the following features.
  The first part of the column can be initialization action.
  The next part of the column can be events handlers that are common for each state.
  The last part of the column is the column state elements.
  An additional section can be added after the column state machines.
  The pseudo initialization and termination events allow substates to be incorporated into a solution.
There are limitation of to column state machine and a more advanced state machine framework is shown here.

## Slide 91: RPC services <back> <next>
  RPC services are CFL instructions which allow columns to act as:
    Servers of Event Requests
    Clients of Event Requests
  RPC
  RPC services have the following CFL instructions.
    For the server:
      store_server_event_process
        This function process
      rpc_event_clean_up
    For the client
      generate_rpc_event
      rpc_client_event_processor

## Slide 92: RPC services <back> <next>
The RPC CFL statements for a server are as follows:
  store_server_event_process(server_fn_name,user_data,rpc_request_list)
    This function processes an RPC event event
    The parameter server_fn_name is the name of the function that processes rpc requests
    The parameter user_data is data for the server function.
    The parameter rpc_request_list is a list of request ids that this server function will respond to.
  For the c implementation, the parameter server_fn_name has the following prototype:
    typedef void (*Server_Process_RPC_event_CFL_t )(const void *input,void *user_data, rpc_rom_message_CFL_t *data);
    The definition of rpc_rom_message is discussed on the next slide.

## Slide 93
This implementation is for a 32K Ram Arm M3 microcontroller.
The structure is broken up into a RAM part and a Flash part.
The RAM part has storage for the received event as well as storage for the event sent back to the client.
The Rom of Flash part of the structure contains the following fields.
  The parameter rpc_request_id. This is the rpc which the message is requesting.
  The unique_id is a sentinel value which is used to verify the message.
  The destination queue is the destination queue of the column where the server column is located.
  The receive queue is the queue for the client column
  The parameter ram message is points to the data structures in the RAM.
typedef struct rpc_ram_message_t
{
Event_data_CFL_t sent_event;
Event_data_CFL_t received_event;
} rpc_ram_message_CFL_t;
typedef struct rpc_rom_message_t
{
unsigned short rpc_request_id;
unsigned short unique_id; // insuring that rpc message is valid
unsigned short destination_queue;
unsigned short receieved_queue;
rpc_ram_message_CFL_t *ram_message;
} rpc_rom_message_CFL_t;

## Slide 94: S Expression Arrays <back> <next>
S Expression Arrays are:
  User defined arrays of fixed length and of the following type:
    Boolean bit
    16-bit integer
    32-bit float
    Other types could be added by user
  Have several built-in operators for these arrays
  Support s expressions for logical and arithmetic operations.

## Slide 95: Uses for CFL S expression arrays <back> <next>
The uses for CFL s expression arrays are two-fold.
  The first use is for data flow programing.
  The second use is to support PLC, Programmable Logic Controller, operations.
In the data flow programming paradigm, a module executes when it receives the necessary information to do so.
The CFL s expression arrays expediates the process of determining execution.
In the CFL system, data flow module is important because the normal control of CFL column is through the control flow of Enable Column type column elements.
Instead, External Columns can decide when to execute. This allows more decentralized construction of systems.
PLC systems will be discussed next.

## Slide 96: PLC operations <back> <next>
The PLC uses arrays of various types to isolate the PLC logic from the underlying hardware as shown in the figure to the right.
Rather than add specific instructions to the PLC logic, the user sets specific array locations.
Some array locations are free to be used by the code writer to implement user logic
Input Bit Array
Relay
16-bit Register Array
Counter
Output Bit Array
Switch
PLC Engine
PLC Source Code

## Slide 97: S Expression Arrays (continued) <back> <next> Ladder Logic vs S Expressions <back> <next>
In many PLC ladder logic expressions are written in the form as shown in the figure to the right as well as the resulting logic expression.
The ladder diagram expressions can be translated into equations as shown in the figure to the right.
However, the CFL system uses s expressions instead of equations. The equivalent s expression is shown in the figure to the right.
The rationale for using s expressions are discussed on the next page.
Bit 1
On
Bit 5
On
Bit 3
Off
Bit 21
On
Motor
Equivalent Logic Expression is
Bit1 and ( not (Bit3) or (Bit 5) ) and Bit21
Equivalent S expression
(and Bit1 (or (not Bit3) Bit5) Bit21)

## Slide 98: Advantages of S Expressions <back> <next>
The advantages of s expressions are as follows:
  S expressions are much easier to parse as s expression do not have operator precedence.
  S expressions can be expanded so that complete programs can be written in s expression.
  Complex programs can be written in s expressions as demonstrated by Lisp and Clojure.
The disadvantage of s expressions is the miss match of the parens in complicated expressions.
  There are CFL auxiliary functions to reduce this complexity.

## Slide 99: S Expression Arrays (continued) <back> <next>
The next section will describe the syntax of the CFL s expressions.
  The form of the CFL s expression is shown below:
    ( function , parameter, …., parameter )
    Where parameter is of three variants
      Scalar value depending on the array type
        For bit array -- bool
        For 16-bit array -- int16_t
        For 32-float array – float
      Value in a buffer array
        Designated by @xxx
        Where xxx is an integer position in the array
        The value of xxx must not exceed the buffer length
      A valid s expression that produces a valid scalar value

## Slide 100: S Expression Arrays (continued) <back> <next>
S expressions are not complete CFL.
Rather s expressions are used for two purposes:
  Generate a value for an array assignment.
  Provide a Boolean result which is used for CFL functions such as
    Wait
    Verify

## Slide 101: Implementation of S expression <back> <next>
Convention s expressions are implemented in the manner of Lisp as a form of linked lists.
For Lisp s expressions are constructed from “cons cells” as shown in the figure on the right.
s expression link lists are usually dynamic memory.
There is two sources of memory loss.
  One from overhead in the heap.
  Another from pointer over head into pointing to values.
Car
Cdr
Value
Pointer to another
cons cell
A cons cell consists of two pointers
Car points to a value
Cdr points to another cons cell

## Slide 102: CFL S expressions support a stack-based approach <back> <next>
Instead, the CFL system stores s expressions as a linear structure and the evaluation of the s expressions as a stack-based approach. The type of s expressions used by the CFL system allows this approach to be used. One of the limitations is that s expressions only return one value.
The CFL assembler transforms the text s expression into the following array of variant records with a tag field.
  The tag field identifies the variant.
  The variant has the following possibilities
    Function id expressed as an integer id
    Buffer position expressed as an integer position
    Value expressed as the type of buffer, i.e., Boolean, integer, float.
    A fourth type is added which is the end of the s expression.
  The CFL assembler checks for valid functions, literal values and buffer positions.

## Slide 103: CFL S Expression run time engine <back> <next>
The figure to the right shows the components of the CFL s expression engine.
The CFL engine reads a CFL s expression stream and does the following functions:
  Store literal values on the parameter stack.
  For array positions, find the array value and store on parameter stack.
  For operator values, store the operator and the current index on the parameter stack on the operator stack.
  For fourth type which is the end of s express, op the operator stack and execute the operator and the parameter stack index. Execute the function where the parameters are from the stack index to the end of the parameter stack. The result is pushed on the parameter stack.
When the s expression ends, both the parameter stack and the operator stack are empty.
The last step is to push the final result on the parameter stack.
Parameter Stack
Operator Stack
CFL engine
CFL S Expression Stream
Operator Stack Entry
Stack
Start
Op
Type

## Slide 104: CFL Stack Approach Consumes Less RAM. <back> <next>
The CFL Stack based approach consumes no persistent RAM.
The RAM that is need is dynamic memory need for the parameter and operator stack for the S Expression Engine.
The CFL assembler will make an estimate of the size of the parameter stack and the operator stack.
  This limits the amount of dynamic memory needed for CFL S Expression calculation.

## Slide 105: S Expression Arrays (continued) <back>
Currently there are 3 valid CFL array types
  The Boolean array type is discussed here.
  The 16-bit integer array helper functions are discussed here.
  The 32-bit float array helper functions are discussed here.

## Slide 106: Bit Register Maps <back> <next>
  Bit Register Maps

## Slide 107: Fixed Point Register Maps <back> <next>
Fixed Point Register Maps

## Slide 108: Float Register Maps <back> <next>
  Float Register Maps

## Slide 109: Complex State Machines <back> <next>
  Complex State Machines

## Slide 111: Appendix A. 32k Ram M0 implementation <back> <next>
TBD

## Slide 112: Appendix A. 32k Ram M0 implementation <back> <next>

## Slide 113: Appendix B. 32k Ram M0 Reprogrammable <back> <next>

## Slide 114: Appendix B. 32k Ram M0 Reprogrammable <back> <next>

## Slide 115: Appendix C. Lua Implementations <back> <next>
The Lua is a heap based dynamic interpretive language. The language consumes more memory than a C implementation. Lua does offer the following advantages.
  A shell-like environment which can offer dynamic scripting.
  More complicated data structures can be added as Lua supports lists and hash tables.
The degree Lua is used in an implementation is due to the trade off due to memory considerations.
The memory profile of Lua is as follows:
  The Lua interpreter will take around a 100k of Flash memory.
  Variables and code are stored in a heap like structure.
  Strings can consume considerable amount of memory of heap memory.

## Slide 116: Appendix C. Lua Implementation <back>
Currently, there are four implementations supported:
  Using Lua as a command shell as shown here.
  Using Lua to initialize and configure a C program as shown here.
  Using Lua to function like micro python as shown here.
  Using Lua on a Linux type processor as shown here.

## Slide 117: Using Lua as a Command Shell <back> <next>
Lua has features shown below which make it ideal for an integrated command shell inside a C program.
  Embeddable in a C program. Many languages like Python, TCL and list are designed to be the main program and C binds to the main program.
  Has easy bindings to C functions as well the ability to easily create new commands.
The utility of Lua as a command shell
  To use a language as a command like shell
  Lua is used to run simple string-based scripts and to call C programs. There are two historical non Lua uses cases.
    I used FICL, a C based Forth implementation to integrate a Cable Modem

## Slide 118: Using Lua as a Command Shell <back> <next>

## Slide 119: Using Lua to initialize and configure a C program <back> <next>

## Slide 120: Using Lua to initialize and configure a C program <back> <next>

## Slide 121: Using Lua to function like micro python <back> <next>

## Slide 122: Using Lua to function like micro python <back> <next>

## Slide 123: Using Lua on a Linux type processor <back> <next>

## Slide 124: Using Lua on a Linux type processor <back> <next>

## Slide 125: Appendix Historical implementation <back> <next>

## Slide 126: Appendix Historical implementation <back> <next>

## Slide 129: Appendix xxxx PLC Background Information <back> <next>
This section describes the following topics
  Historical Background of Discrete Digital Control of Robots
  Introduction of PLC controller
  The need for State Machines
  Stunted Grow of PLC Ladder Logic
  A 1000 Brain Rebirth?

## Slide 130: Appendix xxxx PLC Background Information <back> <next>
In the early 60’s the Auto Industry controlled their robotic machinery, mainly through:
  Low Voltage Relays, ~24 Volts
  Low Voltage Relays could perform logic functions see
    Ladder Logic Boolean Functions
    https://control.com/technical-articles/boolean-logic-for-ladder-diagrams/
  Some Mechanical Features were implemented such as:
    Counters
    Drum CAMS – used for sequencing
    Time Delay Relays

## Slide 131: Appendix xxxx PLC Background Information <back> <next>
The Relay Rails were implemented in Rows from top to bottom as shown on the figure on the right
  The Rails resembled the rungs of a ladder.
  The programming was called Ladder Logic
  Later the Physical Rail size was standardized.
  This standard rail was called Din Rails
  Component manufactures standardized their components to fit the Din Rail dimensions
Mounting Rail
Control Components
Mounting Rail
Control Components
Mounting Rail
Control Components

## Slide 132: Appendix xxxx PCL Background Information <back> <next>
DIN Rail Layout
  The Din Rail layout is divided into two sections
    A Logic Section
    An Output Section
  The Layout can be seen in the figure to the right.
The Role of the Logic Section is to produce a single Boolean Result.
  Logic at any state can be feed into a “sub” rail to handle different logic paths
Mounting Rail
Logic Section
Output Section
Mounting Rail
Sub Rail

## Slide 133: Appendix xxxx PCL Background Information <back> <next>
Based upon the Boolean Result from the Logic Section
  If the result is True
    For Output Relays -- the Relay is turned on
    For Components like Timers
      The function is done
  If the result is False
    For Output Relays -- the Relay is turned off
    For Components like Timers
      The function is not done

## Slide 134: Appendix xxxx PLC Background Information <back> <next>
In the mid 60’s GM developed the concept of a PLC Controller.
  Later these controllers would be reduced to the form of
    Microcontroller based
    Harden I/O to survive the industrial environment
  Programming the PLC controllers resembled the layout of the Analog with pseudo–Analog Components
  By the 2010’s the Programming of the controller was done by
    A PC-based GUI program
    GUI aids to add/delete rails
    Place components on the rail
    Configure placed components
  The component list for the PLCs used on my farm are described in
    https://library.automationdirect.com/wp-content/uploads/2015/07/CLICK-PLC-Instruction-Set-PDF.pdf

## Slide 135: Appendix xxxx PLC Background Information <back> <next>
The PLC implements relays as bit arrays
There are 4 type of PLC memory
  Discrete external inputs to the PLC represented as read only bits
  Discrete external outputs from the PLC represented as read/write bits
  Internal bits for controlling logic of ladder logic programs. These are read/write bits.
  Internal 16 registers for timer counts and other functions. These 16-bit words are read/write 16-bit words

## Slide 136: Appendix xxxx Background Information <back>
The PLC operation is shown in the figure to the right. The PLC operation is a loop which does the following things.
  Read all inputs
  Process all ladder logic operations
    The length of this operation is a function of the number of ladder logic operations.
    Some PLC vendors allow ladder logic “rails” to be attached to interrupt routines to insure real time operations
  The last operation is to write out all outputs from the output bits
Read Inputs
Process outputs
Write Outputs

## Slide 139: NASA VML -- Virtual Machine Language <back> <forward>
This software project since 1997 has been used on
  The large space telescopes
  Juno Probe
  Mars orbiters
  Two Mars Stationary Landers
  And in the future on the
    Small moon landers
    Mars Sample and Return Project
  The software is not open source and is owned by Blue Sun Enterprises
Three papers describe VML environment
  For introduction to the VML architecture
    https://trs.jpl.nasa.gov/bitstream/handle/2014/45392/08-1066_A1b.pdf?sequence=1
    https://www.bluesunenterprises.com/wp-content/uploads/2018/11/Fully-Prog-sc.pdf
  For status of current projects
    https://www.techbriefs.com/component/content/article/tb/spinoff/computer-technology/32690
The next series of slides will describe the architecture

## Slide 140: NASA VML -- Virtual Machine Language <back> <forward>
The VML Architecture consists of
  A series of opcodes running as a virtual machine
  The software executive runs multiple machines running prior mentioned opcodes.
  The VML language compiles into opcodes much like Java
  The VML code is scripts which can be dynamically loaded into virtual machines.
  The VML language is designed to sequence commands that do the intended purpose
  The VML language intent is to separate control from indented action.
The virtual machine layout is shown in the figure to right.
Virtual
Machine
Virtual
Machine
Virtual
Machine
Virtual
Machine
Virtual
Machine
VML
Scripts

## Slide 141: NASA VML -- Virtual Machine Language <back>
On the Pathfinder Lander the VML architecture was tried without a Virtual Machine but embedded in the code using the RTOS, VxWorks.
  The desired effect of separating control logic for action code was not successful.
  Only by separating control and placing it in a “scripting language” did the desired effect result.
Separating Sequencing Control from the Action code and
The sequencing control in scripts allows updates to be transmitted to a spacecraft without the risk of bricking the space craft.

## Slide 142: CFL Assembler Template Language <back> <next>
The CFL statements are written in a scripting language like Lua or Python.
Because of nature of the programming language, macros are not needed much of the time for CFL statements.
However, native code is entered as text and stored by the CFL assembler as text.
For native code, in particular a templating language has been introduced to the offline CFL assembler. Online CFL assemblers do not need the template system.
The template system is described in the following pages.

## Slide 143: Steps in Using CFL Templating Language <back> <next>
The steps in using the template language are as follows:
  Call the initialization function, reset_template_tables.
  Define template variables and template functions.
  Call the function, Expand_text_stream(str) to expand the string str.
The input str consists of free text and template expressions.
Template expression have the following properties.
  The default delimiters of the template expression is “<<“ “>>”, so that the delimiters do not interfere with most code constructs.
  The default delimiters can be changed with the following CFL assembler instruction.
    set_template_marker(start,ending)
  Template expressions can be parameters for template expressions.
The details of template instructions are described on the next page.

## Slide 144: Format of Template Expressions <back> <next>
The format of a template expression is as follows.
  Parameters are separated by either spaces or commas.
  In both cases the leading and trailing spaces are eliminated.
  The first element of a template expression is as a function.
    Functions are added after the initialization call and will be discussed later.
    Only the first parameter can be a function.
    This makes template expressions like s expressions.
    Parameters are either:
      A string
      Template Variable
      Embedded template expressions
    All input strings are queried in a symbol table to detect template variables.
  An example of two template strings are shown here:
    'this is a test <<p_l, - ,a,"b","c" >> <<p,a>> result’
      This expression uses commas to separate parameters
    'this is a test <<p_l, - a "b" "c" <<p b>> >> <<p,a>> result’
      This expression uses spaces to separate the parameters
      This expression also has an embedded template expression in the parameter stream

## Slide 145: Property of template functions: <back> <next>
A template function is written in the base language of the CFL assembler, which is currently Lua.
The prototype is of a template function is of the following form.
  function xxx(parameter_1 , …., parameter_n)
  Inputs of the template expression are passed to the function.
  If the number of parameters passed is less than parameter_n then nils are passed to the remaining parameters to the function.
  If the number of parameters is greater that than parameter_n, then the remaining input parameters are ignored.

## Slide 146: Actions when template engine is reset <back> <next>
To use the CFL templating system, the environment needs to be initialized. This is done first be calling the function reset_template_tables. The function does the following actions.
  function_table = {}
  variable_table = {}
  function_table['p_l'] = output
  function_table['p'] = dump
This function clears the function and variable tables and defined two default functions.
The two default functions will be defined here.

## Slide 147: How to add template variables and functions <back> <next>
After the reset is called, the user can add template variables with the following statement:
  variable_table[“parameter_name”] = string_value
When ever a template parameter “parameter_name is found, the value of string_value is replaced.
Similarly, template functions can be added by the following statement:
  Function_table[“function_name”] = <function variable>
The function table will be accessed on the evaluation of the first parameter. If the function name is not found in the function table, then an error is posted.
Parameters passed to the template functions will be strings.
  If the parameters are template variables, then the template variables will be expanded to their underlying strings.

## Slide 148: Default template functions <back> <next>
The two default template functions are:
  Function p, returns the first parameter as a string.
    This function is useful for dumping template variables into the string.
  Function p_l, does the following actions:
    The first parameter is a token.
    The output of the function is a concatenation of the parameters with the separator being the token, which is the first parameter.
The next page shows examples using the templating language.

## Slide 149: Template Example <back> <next>
Input
reset_template_tables()
variable_table['a'] = "1"
variable_table['b'] = "2"
str = "this is a test"
print("input is ",str)
result = Expand_text_stream(str)
print("result is ",result)
str = 'this is a test <<p_l, - ,a,"b","c" >> <<p,a>> result'
print("input is ",str)
result = Expand_text_stream(str)
print("result is ",result)
str = 'this is a test <<p_l, - a "b" "c" <<p b>> >> <<p,a>> result'
print("input is ",str)
result = Expand_text_stream(str)
print("result is ",result)
Output
input is this is a test
result is this is a test
input is this is a test <<p_l, - ,a,"b","c" >> <<p,a>> result
result is this is a test 1-"b"-"c" 1 result
input is this is a test <<p_l, - a "b" "c" <<p b>> >> <<p,a>> result
result is this is a test 1-"b"-"c"-2 1 result

## Slide 150: Example showing the change of token markers <back>
Test with change of token markers
Input
set_template_marker("<{","}>")
reset_template_tables()
variable_table['a'] = "1"
variable_table['b'] = "2"
str = "this is a test"
print("input is ",str)
result = Expand_text_stream(str)
str = 'this is a test <{p_l, - ,a,"b","c" }> <{p,a}> result'
print("input is ",str)
result = Expand_text_stream(str)
print("result is ",result)
str = 'this is a test <{p_l, - a "b" "c" <{p b}> }> <{p,a}> result'
print("input is ",str)
result = Expand_text_stream(str)
print("result is ",result)
Output
Same as default token markers
result is this is a test
input is this is a test <{p_l, - ,a,"b","c" }> <{p,a}> result
result is this is a test 1-"b"-"c" 1 result
input is this is a test <{p_l, - a "b" "c" <{p b}> }> <{p,a}> result
result is this is a test 1-"b"-"c"-2 1 result